## Slide 1
Congestion Control in Datacenter Based on Both RTT and ECN
Liang Junpeng, 2014050690
Supervisor: Cui Lin

## Slide 2
TCP Problems in Datacenter
01
Existing Congestion Control Algorithm for Datacenter Network
02
Introduction to T-DCTCP
03
Performance of T-DCTCP
04
Conclusion
05
CONTENTS

## Slide 3
TCP Problems in Datacenter
01
The sources of incompatibility between TCP and Datacenter
Distributed computation model:
Partition/Aggregate
Using switches with shallow buffer
Using shared-buffer switches

## Slide 4
TCP Problems in Datacenter
01
The incompatible issues between TCP and Datacenter
TCP incast issue
TCP outcast issue (queue buildup)
These two issues can have great harm to network performance, like decreasing throughput and increasing latency.

## Slide 5
Existing Congestion Control Algorithm for Datacenter Network
02
DCTCP (SIGCOMM 2010);
MCP (ACM HotNets-XII 2013);
DT-DCTCP (IEEE ICDCS 2013);
Congestion Control based on ECN
TCP-FITDC (ICNC 2013);
NewTCP (IEEE ICC 2014);
TIMELY (SIGCOMM 2015);
DX (USENIX 2015);
Deadline-aware congestion control: D2TCP (SIGCOMM 2012)
Congestion control based on window size notification: TCP-CWR (ITC 2013)
Congestion Control based on other indicator
Congestion Control based on RTT

## Slide 6
Introduction to T-DCTCP
03
Motivation of choosing both ECN and RTT
ECN is single-bit congestion signal.
RTT is not precise enough at controlling congestion window.
Bad handle on packet burst.
Poor performance in congestion window adjustment.
Drawback
We would like T-DCTCP can just modify senders and receivers instead of switch
EAR
Modification on switches.

## Slide 7
Introduction to T-DCTCP
03
Eight situations for modifying congestion window
New RTT is less than Tlow
New RTT is greater than Thigh
RTT is decreasing
RTT is increasing
1
alpha is less than alpha_factor
2
alpha is greater than alpha_factor
S
Alpha is calculated from the fraction of the ACKed packets with ECN flag
alpha_factor is a self-defined parameter
normalized_gradient equals to the difference of RTTs divided by minimum RTT to remove its unit. It reveals the trend of RTT.
1. cwnd increases by addstep
2. cwnd decreases slightly according to alpha
1. cwnd decreases according to the value exceeding Thigh and the value of alpha
2. cwnd decreases by half
1. cwnd increases by addstep
2. cwnd decreases slightly according to alpha
1. cwnd decreases according to the value of normalized_gradient
2. cwnd decreases according to alpha

## Slide 8
Performance of T-DCTCP
04
Network Experiment Topology
Mininet
Use iperf to simulate incast issue
Use curl to simulate incast issue with various flow sizes in different qunanities
Incast simulation

## Slide 9
Performance of T-DCTCP
04
The throughputs of T-DCTCP and DCTCP are close.
The throughput of T-DCTCP is 2% smaller than that of DCTCP
Comparing throughput
The average RTT of T-DCTCP is 9.4% smaller than the average RTT of DCTCP, and is 143.2% smaller than that of TCP with CUBIC.
As for 99th percentile RTT, T-DCTCP drops it by 37.7% and 123.2% comparing to DCTCP and TCP with CUBIC.
CDF diagram of RTT

## Slide 10
Performance of T-DCTCP
04
The blue curve represents T-DCTCP and it rises faster than the orange one.
In 80th percentile, FCT of T-DCTCP is 10% smaller than that of DCTCP.
CDF diagram of FCT
  FCT of 2KB flow is 1.4X smaller.
  FCT of 50KB flow reduces by 31%.
  FCT of 1MB flow drops by 48.2%.
  FCT of 10MB flow increases slightly.
Bar diagram of FCT

## Slide 11
Conclusion
05
T-DCTCP does reduce RTT without decrease on throughput.
T-DCTCP does improve FCT of small flows.
T-DCTCP reveals the feasibility of using both RTT and ECN as congestion indicators to control congestion level.
Future work: We can try to improve RTT measurement accuracy and find a better way to describe congestion and a better scheme to control cwnd.

## Slide 12
That’s all of my presentation
Expecting your advice on T-DCTCP